## Slide 1: Chapter 3:
DIGITAL LOGIC DESIGN ( ce_118 )
Register Transfer
Specification & Design
(part_2)

## Slide 2: Outline
Register Transfer (RT) design:
  FSMD model
  RT specification with
    Static-action tables
    ASM charts
Procedure for synthesis from RT specification
Design Optimization through
  Register sharing
  Functional unit sharing
  Bus sharing
  Unit chaining and Multiclocking
Design Pipelining
  Unit pipelining
  Control pipelining
  Datapath pipelining
Scheduling of flowcharts
Notes: Các kiểu Mergin có tính kế thừa và liên tục

## Slide 3: Register-transfer synthesis (synthesis from ASM chart)
ASM Chart of Square-root approximation
Register sharing
Functional unit sharing
Bus sharing (datapath conectivity)
max((0,875x+0,5y),x)
where x = max (a,b)
y = min (a,b)
Notes: 0.875*x = x – 0.125*x = x – x>> 3
0.5y = y*2^-1 = y >> 1

## Slide 4: Resource usage in square-root approximation
Variable usage (register/memory sharing)
ASM Chart of Square-root approximation
Operation usage (functional-unit sharing)

## Slide 5: Connectivity requirements
Connectivity table (bus sharing)
ASM Chart of Square-root approximation

## Slide 6: Simple library components
a) Absolute value unit (version 1)
(c) Min unit
(d) Max unit
(e) Min/Max unit
b) Absolute value unit (version 2)

## Slide 7: Simple library components (cont.)
(f) 1-bit right shifter
(g) 3-bit right shifter
(h) 1-bit/3-bit right shifter
(i) Adder
(j) Subtractor
(k) Adder/Subtractor

## Slide 8: Register sharing (Variable merging)
Grouping of variables with non-overlapping lifetimes in a register
Variables that are not used (write or read) in the same state are called non-overlapping lifetime variables.
Lifetime of a variable: set of states in which the variable is alive. It is from the first state that the variable is written (write state) to the last state that variable is used (read state), include all states between the first and last state.
Grouping reduces number of registers needed in the design  Reduce area and cost
Two algorithms:
  left-edge
  graph-partitioning

## Slide 9: Left-edge algorithm
Create variables usage table
Sort list of variables

## Slide 10: Register sharing with left-edge algorithm
Sorted list of variables
Priority order for 2 variables have the same write state:
The variable with the longer lifetime
The priority will be assigned at random
Variable usage table
Creating priority list
Notes: Nếu 2 biến cùng xuất hiện trên 1 state thì biến nào tồn tại lâu hơn thì xếp trên

## Slide 11: Register sharing with left-edge algorithm
Left-edge algorithm
Sorted list of variables
R1 = {a, t1, x, t7}
R2 = {b, t2, y, t4, t6}
R3 = {t3, t5 }
Register assignments
Datapath schematic
a
t1
x
t7
b
t2
y
t4
t6
t3
t5

## Slide 12: Compatibility graph for register sharing
Compatibility graph: nodes and edges
- Node represents a variable
- Edge: incompatibility edge and priority edge
+ Incompatibility edge (dashed line): connect 2 nodes indicates 2 variables with overlapping lifetimes
+ Priority edge: connect 2 nodes indicates 2 non-overlapping lifetime variables that serve as the same source (input) or same destination (output) to the same functional units or units in used library.
Priority weight (s/d) on priority edge: the number of selector inputs can be saved
s is equal to the number of the same functional units that use both nodes as right operands (input).
d is equal to the number of the same functional units that generate results (output) for both nodes
(Variables) compatibility graph

## Slide 13: Graph-partitioning algorithm
(a) Initial (varialbes) compatibility graph
Variable usage (register/memory sharing)
ASM Chart (square-root approximation)
Notes: t1, x are all inputs of the same MIN/MAX unit (1/0): do cả t1 và x đều là toán hạng bên phải (inputs) của phép cộng/trừ nên s=1 (nếu t1 và x đều là toán hạng của một phép khác, vd add/sub thì giá trị s sẽ được cộng thêm). Do t1 và x không là kết quả (outputs) của chung phép toán nào nên d = 0
t2, x are all inputs of the same MIN/MAX unit (1/0)
t1, t6 are all inputs of the same MIN/MAX unit (1/0)
t2, t6 are all inputs of the same MIN/MAX unit (1/0)
x, t7 are all outputs of the same MIN/MAX unit (0/1). Do x và t7 đều là kết quả (outputs) của bộ MIN/MAX nên d = 1
y, t7 are all outputs of the same MIN/MAX unit. (1/0)
t3, t5 are all inputs of the same SUB/ADD unit (0/1). Do t3 và t5 đều là kết quả (outputs) của bộ SUB/ADD nên d = 1
t5, t6 are all outputs of the same SUB/ADD unit (0/1). Do t5 và t6 đều là kết quả (outputs) của bộ SUB/ADD nên d = 1

## Slide 14: Graph-partitioning algorithm for SRA
Initial compatibility graph
(b) Compatibility graph after merging t3, t5 and t6
(c) Compatibility graph after merging t1, x and t7
ASM Chart

## Slide 15: Graph-partitioning algorithm for SRA
ASM Chart
(d) Compatibility graph after merging t2 and y
(e) Final compatibility graph

## Slide 16: Register assignment generated by the graph-partitioning algorithm
Datapath
R1 = [a , t1 , x , t7]
R2 = [b , t2 , y , t3 , t5 , t6]
R3 = [t4]
Register assignments
Compare selector input numbers with Datapath generated by the left-edge algorithm??? (slide 11)

## Slide 17: Functional-unit sharing (operator merging)
Group non-concurrent operations
Each group shares one functional unit
Sharing reduces number of functional units
Prioritized grouping by reducing connectivity
Clustering algorithm used for grouping

## Slide 18: Functional-unit sharing
Partial ASM Chart
Non-shared design
Shared design
-

## Slide 19: Complex library components
Unit for computing minimum,
maximum and absolute value
Unit for computing addition,
subtraction, minimum and maximum
Unit for computing addition,
subtraction, and absolute value
Unit for computing addition, subtraction,
minimum, maximum and absolute value

## Slide 20: Operator merging for SRA implementation
ASM Chart
Compatibiltity graph
(single function unit)
(c) Merging altermative
(simple merging operator)
(e) Merging altermative
(simple merging operator)
(b) Cost table graph (a)
(d) Cost table graph (c)
(f) Cost table graph (e)
Notes: Cost table graph (c) trên slide/trong sách bị sai
[|a|, min] 1 1 0 1 2
Sửa: [|a|, max] 1 2 0 1 2

## Slide 22: Datapath connectivity
ASM Chart
Datapath schematic
Compare selector input numbers with Datapath in slide 17???
(c) Merging altermative
(simple merging operator)
R1 = [a , t1 , x , t7]
R2 = [b , t2 , y , t3 , t5 , t6]
R3 = [t4]
Notes: Datapath trên slide/trong sách bị sai
Sửa: [abs/min]  [abs/max]; [abs/max/+/-]  [abs/min/+/-]

## Slide 23: Datapath connectivity
ASM Chart
Datapath schematic
Compare selector input numbers with Datapath in slide 17 ???
(e) Merging altermative
(simple merging operator)
R1 = [a , t1 , x , t7]
R2 = [b , t2 , y , t3 , t5 , t6]
R3 = [t4]

## Slide 24: Priorities in unit merging
(a) Partial ASM Chart
(b) Design without merged units
(c) Design with merged units

## Slide 25: Compatibility graph for functional-unit sharing
(Operators) compatibility graph
Compatibility graph: nodes and edges
- Node represents a operator
- Edge: incompatibility edge and priority edge
+ Incompatibility edge (dashed line): connect 2 nodes indicates 2 operators that are occurred concerrently in the same state.
+ Priority edge: connect 2 nodes indicates 2 operators that have the operator’s similarity in construction (depend on component libraries) or the substantially reduce the cost (depend on priority weight) of the datapath’s connection.
Priority weight (s/d) on priority edge: the number of connections can be saved
s is equal to the number of common sources between two operators
d is equal to the number of common destinations between two operators.
Note: If the ASM chart has more than one operator (e.g max) in ASM chart, the maximum value of s or d from each one to other operator will be chosen.

## Slide 26: Unit merging for SRA datapath
ASM Chart
(Operators) Compatibility graph
Register assignment in register sharing with graph-partitioning algorithm (slide16)
R1 = [a , t1 , x , t7]
R2 = [b , t2 , y , t3 , t5 , t6]
R3 = [t4]
Notes: Dựa vào các thanh ghi R1, R2, R3 của phương pháp phân hoạch đồ thị

## Slide 27: Unit merging for SRA datapath
ASM Chart
(a) Compatibility graph
(b) Compatibility graph
after merging of + and – (operator’s similarity grouping)
(d) Final graph partitions
(datapath’s connection grouping)
(c) Compatibility graph
after merging of min, + and –
(datapath’s connection grouping)
Sách sai
Notes: Operator’s similarity grouping: group theo cùng chức năng
Datapath’s connection grouping: group theo ưu tiên số lượng lớn connection
 Trong thực tế thì group theo cả 2 cách trên

## Slide 28: SRA datapath generated by prioritized partitioning (use register and functional-unit sharing)
R1 = [ a, t1, x, t7 ]
R2 = [ b, t2, y, t3, t5, t6 ]
R3 = [ t4 ]
AU1 = [ |b| / min / + / - ]
AU2 = [ |a| / max ]
SH1 = [ >>1 ]
SH2 = [ >>3 ]
(b) Datapath schematic
(a) Register and functional unit allocation
Compare selector input numbers with Datapath in slide 17,22,23 ???

## Slide 29: Bus sharing ( connection merging )
Group connections that are not used concurrently
Each group forms a bus
Connection merging reduces number of wires
Clustering algorithm is demonstrated

## Slide 30: Compatibility graph for bus sharing
(connection) compatibility graph
Compatibility graph: nodes and edges
- Node represents each connection
- Edge: incompatibility edge and priority edge
+ Incompatibility edge (dashed line): connect 2 nodes whenever their corresponding connections do not originate from the same source, but are used at the same time.
+ Priority edge: connect 2 nodes whenever their corresponding connections have a common source or a common destination.
Priority weight (s/d) on priority edge: No  using a graph-patitioning algorithm to group connections in a way that will maximize the number of priority edges included in all groups.
Connection sources: outputs of register and functional units / input of circuit
Connection destinations: inputs of register and functional units

## Slide 31: Connection merging in SRA datapath
(b) Connectivity usage table
ASM Chart
R1 = [a, t1, x, t7]
R2 = [b, t2, y, t3, t5, t6]
R3 = [t4]
Notes: Connection sources: outputs of register and functional units / input of circuit
Connection destinations: inputs of register and functional units
Cách tạo ra Connectivity usage table:
Ví dụ xét tại state s1:
Sử dụng khối tính |a| và khối |b|
Khối |a| nằm trong khối [abs/max], mà giá trị input a thì xuất phát từ thanh ghi R1, nên C là một connection source
Khối |b| nằm trong khối [abs/min/+/-], mà giá trị input b thì xuất phát từ thanh ghi R2, nên F là một connection source
I là một output của khối [abs/max] và là input của R1, nên I là một connection destination
J là một output của khối [abs/min/+/-] và là input của R2, nên J là một connection destination
Như vậy đối với state s1, sử dụng các connections sau: C, F, I, J
Làm tương tự cho các state khác

## Slide 32: Connection merging in SRA datapath
(b) Connectivity usage table
(c) Compatibility graph
for input buses (AU and SH inputs)
(d) Compatibility graph
for output buses (AU and SH outputs)
R1 = [A, C, D, H]
R2 = [B, F, G]
R3 = [E]
Sách sai
Notes: - Edge: incompatibility edge and priority edge
+ Incompatibility edge (dashed line): connect 2 nodes whenever their corresponding connections do not originate from the same source, but are used at the same time.
+ Priority edge: connect 2 nodes whenever their corresponding connections have a common source or a common destination.

## Slide 33: Connection merging in SRA datapath
(c) Compatibility graph
for input buses
(d) Compatibility graph
for output buses
Bus1 = [ A, C, D, E, H ]
Bus2 = [ B, F, G ]
Bus3 = [ I, K, M ]
Bus4 = [ J, L, N ]
(e) Bus assignment

## Slide 34: Connection merging in SRA datapath
Bus assignment
(f) Bus oriented datapath
Bus1 = [ A, C, D, E, H ]
Bus2 = [ B, F, G ]
Bus3 = [ I, K, M ]
Bus4 = [ J, L, N ]
Đổi thành

## Slide 35: Register merging
Group register with non-overlapping accesses
Each group assigned to one register file
Register grouping reduces number of ports, and therefore number of buses
Demonstration with clustering algorithm

## Slide 36: Register merging
ASM Chart
R1 = [ a, t1, x, t7 ]
R2 = [ b, t2, y, t3, t5, t6 ]
R3 = [ t4 ]
(a) Register assignment
(b) Register access table
(c) Compatibility graph
(d) Datapath schematic
Ko cần TRI ở đây

## Slide 37: Bài tập
Viết chương trình tạo datapath tính tổng a2i (i = 1 .. 100).
  Viết giải thuật bằng mã giả.
  Chuyển mã giả sang sơ đồ ASM.
  Lập bảng trạng thái
  Chia sẻ thanh ghi? (nếu có).
  Chia sẻ chức năng? (nếu có).
  Chia sẻ bus? (nếu có).